## Slide 1: Cansat in Russia
Team name is KYYRAI
Performed by student of 11th grade
Popov Vladimir
Teacher: Nyurgun Maratovich
Yakutsk city – 2019 year

## Slide 2
Team leader
(Popov Vladimir)
Alternate
team leader
(Marat Efimovich)
Scientific leader
(Nuyrgun Maratovich)
Electronic
Programmer
Mechanic
Antonov Alexey
Popov Vladimir
Team list:

## Slide 3: Designer
Mechanical frame
Three boards
Charge MC Atmega128
Board of science load (temperature sensor, pressure and accelerometer.
Board of radio-module(transceiver) , frequency – 2,4 -2,525 GHz.
Satellite Cansat consists of:

## Slide 4: Missions of my spacecraft
My main mission is a ecological monitoring.
I will be watching the concentration of dust in the air.
My device measures the amount of dust in the air (mg/m^3)
I want to make our city ecologically safe.

## Slide 5: Our missions:
Measurement of temperature and pressure on the descent path.

## Slide 6
2. Data acquisition and interpretation with 3-axis accelerometer.

## Slide 7
3. Construction of the trajectory of the satellite descent from the data obtained.

## Slide 8
4. Humidity measurement
Chart: 
| Влажность
 | 0.3 | 0.33 | 0.38 | 0.42 | 0.5 | 0.56 | 0.6 | 0.65 | 0.72 | 0.83

## Slide 9
5. Surveying the area

## Slide 10
6. Measuring the amount of dust

## Slide 11
7. Transmissions of telemetry over the radio channel to the ground receiving station.

## Slide 12
Flight diagram

## Slide 13
The block-diagram of the satellite:
Microcontroller
(Atmega128)
Press/Temp
Camera
Accelerometer
Gps-module
Dust sensor
Battery
Ground station
antenna
receiver
PC
Data
Power
antenna
receiver

## Slide 14
Project work
Radio module board
MC board Atmega128
Sensor board
Camera lens
GPS-module
Dust sensor
Battery
Camera

## Slide 15
Monitoring of dust concentration:
X
Y
Z
W
F

## Slide 16
What we used:
We use C language for programming our device.
Our device differs from the standart in that it has a built-in dust sensor, camera and Gps-module.

## Slide 17
System of safety:
Hemisphere type system of safety
F= the force of air resistance
r = radius of parashute
r
F=mg
Fc=mg-ma

## Slide 18
The calculation of the parachute canopy:
m= 0.35 кг– weight of the device
g= 9.8 м/с2 - acceleration of gravity
cd= 1.2– drag coefficient
ρ=1.2754 кг/м3 – air density
v=8 м/с – the speed of descent
r= 15 см – the radius of the base of the parachute
D= 30 см – the diameter of the parachute.
F= the force of air resistance.
Hemisphere type system of safety

## Slide 19
Device | Voltage (V) | Amperage(А) | Power(W)
GPS NEO-6M | 3,30 | 0,10 | 0,33
BMP280- | 5,00 | 0,00 | 0,01
GP2Y1010AU0F | 5,00 | 0,02 | 0,10
DS18B20 | 5,00 | 0,00 | 0,01
Atmega128 | 5,00 | 0,02 | 0,10
ADXL345- | 3,60 | 0,00 | 0,00
E01-ML01SP2 | 3,60 | 0,02 | 0,10
DHT11 | 5,00 | 0,20 | 0,10
Итог | 35,5 | 0,36 | 0,75

## Slide 20: Dust sensor - GP2Y1010AU0F
Supply voltage: 5-7V operating temperature: -10-65 ° C consumption Current: 20mA max minimum detectable particle Size: 0.0008 mm Sensitivity: 0.5 V / (0.1 mg / m3)
clean air voltage: 0.9 V
storage Temperature: -20 ~ 80 ℃
Size: 46mm × 30mm × 17.6 mm

## Slide 21
The Sharp GP2Y1010AU0F optical dust sensor is effective in detecting very fine particles, and is commonly used in air purification systems. The infrared diode and phototransistor are located diagonally and contribute to the detection of reflected light of dust particles in the air. The sensor has a very low power consumption (20 mA maximum, 11 mA average). The output signal of the sensor is an analog voltage proportional to the measured dust density

## Slide 22
Microcontroller
Atmega128:
128KB reprogrammable flash memory
4KB flash memory for data
4KB of RAM
The supply voltage of 5V

## Slide 23
- Основные аппаратные интерфейсы
- TWI (Two-wire Serial Interface)
- USART (Universal Synchronous and Asynchronous serial Receiver and Transmitter
- The 16-bit Timer/Counter
- 53 Programmable I/O Lines
Microcontroller:

## Slide 24
Calibrated digital thermometer with 9 to 12 bit resolution (resolution 0.0625 With) Communicates over the 1-Wire bus and thus can be as the only device on the line TC and work in a group Supply voltage 3 to 5.5 V Measurement accuracy +-0.5 S in the range from-10S to + 85S To start the measurement, you must submit the start command (0x44) After the conversion, the received data is stored in the 2-byte temperature register in the RAM and the DS18B20 returns to the inactive state. Maximum measurement time 750ms
Temperature sensor:

## Slide 25
Module supply voltage: 3.3 V or 5V DC (both levels are supported). Current consumption: up to 2 mA during measurements (depends on accuracy mode). Current consumption: up to 0.2 mA in standby mode. Measured pressure: 30 '000 to 110'000 PA (resolution 0.16 PA) Measured temperature: 0 to +65 °C (resolution 0.01°C) I2C bus operating frequency: up to 3.4 MHz. The address of the module on the I2C bus: 0x77. Logic level "1" on the I2C bus: 0.7*Vcc to Vcc (where Vcc is the supply voltage of the module) Preparation for the first start after power supply: at least 2 MS. Operating temperature: -40 ... +85 °C Dimensions: 30x30 mm
Pressure sensor:

## Slide 26
Supply voltage from 2 to 3.6 volts Current consumed in the operating mode from 40 to 150 microA, depending on the polling frequency Resolution from 10 to 13 bits 3 axis accelerometer Operating temperature range -40 to + 85 degrees Celsius Digital interfaces SPI (three - or four-wire) and I2C Detection of events: push, double push, free fall, the presence of activity along the axes, the lack of activity 2 programmable event outputs The LGA package measuring 3×5×1 mm Shock resistant with accelerations up to 10000G
Accelerometer ADXL345:

## Slide 27
[IC]: nRF24L01P
[Frequency]: 2.4 ~ 2.525 GHz
[Power]: 20 dBm
[Distance]: 1.8 km
[SPI] interface
[Introduction]: E01-ML01SP2 is based on the original imported nrf24l01p Nordic form in Norway. And equipped with a 20 dBm power amplifier chip imported from the US, through which the transmission power reaches 100mW (20 dBm). Professional hardware design allows the use of small size module, which is convenient for all kinds of built-in sensors.
Radio-module E01-ML01SP2 :

## Slide 28
Supply voltage: 3-5V
Positioning accuracy: up to 5m
"Hot start": 1 s
Tracking sensitivity : -162 dBm
Location update rate: 5Hz
Temperature range: -40 to 85°C
Antenna size: 18x18 mm Module size: 22x30x13mm
Gps-module NEO-6M:

## Slide 29
Thanks for waching!
Спасибо за внимание!
Кербуккутун иhин махтал!
Gracias por su atención!